CH-C-0001-0001                    * CH-C-0001-0001 is a Hall-Effect current transducer.

Current Transducer                              * It can be used for the detection of DC, AC, pulse.

| Electrical data |
| --- |
| IPN | Primary nominal r.m.s current |  |  |  | 1 | A |
| IP | Primary current, measuring range |  |  |  | 0…( 1.5 | A |
| ISN | Secondary nominal r.m.s current |  |  |  | 25 | mA |
| VC | Supply voltage (( 5%) |  |  |  | ( 15 | V |
| IC | Idle Current consumption |  |  |  | 15(@( 15) | mA |
| Vd | AC isolation test, 50 Hz, 1min |  | 3 | kV |
| RM | Measuring resistance @ | TA = 100(C |  |  |
|  |  |  | RM min |  | RM max |  |
|  | with ( 15V | @(1Amax | 200 |  | 550 | ( |
|  |  | @(1.5Amax | 150 |  | 360 | ( |

| Accuracy – Dynamic performance data |
| --- |
| X | Accuracy @ IPN , TA = 25(C | @ ( 15V (( 5%) | (( 0.40 | % |
| (L | Linearity |  | < 0.15 | % |
| IO | Offset current @ IP = 0, TA = 25(C @(100 Amax 0 0 | ( 0.15 |  | mA |
| IOM | Residual current @ IP = 0, after an overload of 3 ( IPN 0 |  | ( 0.20 | mA |
| IOT | Thermal drift of IO @(100 Amax | (0℃…+100℃) | ( 0.35 |  | mA |
| tr | Response time @ 90% of IPN |  |  |  | <3 | (s |
| di/dtt | di/dt accurately followed |  | >100 | A/us |
| f | Frequency bandwidth (-1 dB) |  | DC…100 | kHz |

| General data |
| --- |
| TA | Ambient operating temperature |  | -10..+100 | (C |
| M | Mass |  | 20 | g |

Remarks

- IS is positive when Ip flows from terminals +HT to –HT.

- This is a standard model .For different versions (supply voltages,turns ratios,unidirectional measurements….), please contact us.

# Text boxes

IPN = 1 A

Applications

- AC variable speed drives and servo motor drives

- Static converters for DC motor drives

- Battery supplied applications

- Uninterruptible Power Supplies(UPS)

- Switched Mode Power Supplies (SMPS)

- Power supplies for welding applications.

Features

- Closed loop (compensated) current transducer using the Hall-Effect

Advantages

- Excellent accuracy

- Very good linearity

- Low temperature drift

Special features

- Connection to secondary circuit

on 2510-3Y connector.

## SECONDARY TERMINALS

TERMINAL  M: MEASURE

TERMINAL  - :SUPPLY VOLTAGE –15V

TERMINAL  + :SUPPLY VOLTAGE +15V

TERMINAL  +HT: IN

TERMINAL  -HT: OUT