Voltage Transducer CH-C-0025-0009

* CH-C-0025-0009 is a Hall-Effect voltage transducer.

* It can be used for the detection of DC, AC, pulse.

| Electrical data |
| --- |
| IPN | Primary nominal r.m.s current | 10 | mA |
| IP | Primary current, measuring range | 0…( 14 | mA |
| RM | Measuring resistance @ TA = 100(C |
|  |  | RM min | RM max |  |
|  | with ( 12 V | @(10mAmax | 30 | 336 | ( |
|  |  | @(14mAmax | 30 | 214 | ( |
|  | with ( 15 V | @(10mAmax | 40 | 440 | ( |
|  |  | @(14mAmax | 40 | 286 | ( |
| ISN | Secondary nominal r.m.s current | 25 | mA |
| KN | Conversion ratio | 2500 :1000 |  |
| VC | Supply voltage (( 5%) | ( 12…15 | V |
| IC | Idle current consumption | 10(@(15V)+Is | mA |
| Vd | AC isolation test, 50 Hz, 1min | 2.5 | kV |

| Accuracy – Dynamic performance data |
| --- |
| X | Accuracy @ IPN , TA = 25(C, f=1kHz @ ( 12.. (15V, | ( ( 0.9 | % |
|  | @(15V,( ( 5%) | (0.8 | % |
| (L | Linearity | < 0.2 | % |
| IO | Offset current @ IP = 0, TA = 25(C @(100 Amax 0 0 | ( 0.15 | mA |
| IOM | Residual current @ IP = 0, after an overload of 3 ( IPN 0 | ( 0.20 | mA |
| IOT | Thermal drift of IO (0℃…+100℃) @(100 Amax | ( 0.35 | mA |
| tr | Response time @ 90% of Vpmax | <40 | (s |
| di/dt | di/dt accurately followed | >100 | A/(s |
| f | Frequency bandwidth (-1 dB) | DC…100 | kHz |

| General data |
| --- |
| TA | Ambient operating temperature | -10..+100 | (C |
| RP | Primary coil resistance@ TA = 25(C | 113 | Ω |
| RS | Secondary coil resistance @TA = 25(C | 47 | Ω |
| M | Mass | 20 | g |

Mechanical Characteristic:  General tolerance  ±0.1mm

Notes:  For voltage measurements ,a current proportional to the measured voltage must be passed through an external resistor R1 which is selected by the user and installed in series with the primary circuit of the transducer .And the primary resistor  R1: the transducer’s optimum accuracy is obtained at the nominal primary current. As far as possible, R1 should be calculated so that the nominal voltage to be measured corresponds to a primary current of 10mA.

Example: Voltage to be measured VPN =250V

a).R1=25KΩ/2.5W, IP =10mA    Accuracy=±0.8% of VPN (@TA =+25(C)

b).R1=50KΩ/1.25W, IP =5mA    Accuracy=±1.6% of VPN (@TA =+25(C)

##### Remarks

- Is is positive when Vp is applied on terminal +HT.

- This is a standard model .For different versions (supply voltages,turns ratios,unidirectional

measurements….), please contact us..

# Text boxes

Advantages

- Excellent accuracy

- Very good linearity

- Low temperature drift

Special features

● Printed circuit board mounting.

Features

- Closed loop (compensated) voltage transducer using the Hall-Effect

IPN =10mA

Advantages

- Excellent accuracy

- Very good linearity

- Low temperature drift

- No insertion losses

- High immunity against external interference

- Current overload capability

Features

- Closed loop (compensated) current sensor using the Hall-Effect

- Printed circuit board mounting

- Insulated plastic case recognized according to UL 94-V0

Applications

- AC variable speed drives and servo motor drives

- Static converters for DC motor drives

- Battery supplied applications

- Uninterruptible Power Supplies (UPS)

- Power supplies for welding applications.