CH-C-0025-0201                    * CH-C-0025-0201 is a Hall-Effect current transducer.

Current Transducer                              * It can be used for the detection of DC, AC, pulse.

| Electrical data |
| --- |
| IPN | Primary nominal r.m.s current |  |  |  | 25 | A |
| IP | Primary current, measuring range |  |  |  | 0…( 75① | A |
| Vout | Analog output voltage @ Ip Ip=0 | 2.5±(0.625·IP / IPN) | V |
|  | Ip=0 | x | 2.5±0.025② | V |
| Ns | Number of secondary turns ((0.1%) | 2000 |  |  |
| RL | Load resistance | ≥2 |  | k( |
| VC | Supply voltage (( 5%) |  | 5 | V |
| IC | Current consumption @ VC =5V |  | 20 | mA |
| Vd | r.m.s voltage for AC isolation test, 50 Hz, 1min | 3 | kV |

| Accuracy – Dynamic performance data |
| --- |
| X | Accuracy @ IPN , TA = 25(C | 5V (( 5%) | ( 0.20 | % |
|  | Accuracy with RIM @ IPN,TA=25(C |  | ( 0.60 | % |
| (L | Linearity error |  | < 0.15 | % |
| TCVOUT | Thermal drift of VOUT / VREF @ IP=0 -10(C..+100(C | 50 | Ppm/K |
| TCVG | Thermal drift of the gain -10(C..+100(C | 50 | Ppm/K |
| VOM | Residual voltage @ Ip=0,after an overload of 3 x IPN | ( 0.4 | mV |
| tr | Response time @ 90% of IPN | <200 | ns |
| di/dt | di/dt accurately followed | >100 | A/(s |
| f | Frequency bandwidth(-1dB) | DC..200 | kHz |

| General data |
| --- |
| TA | Ambient operating temperature |  | -10..+100 | (C |
| m | Mass |  | 12 | g |

Notes: ① Only in refout mode or with external REF  less than 2.525V and greater than 2.475V .;② VOUT is linked to VREF ,by conception the difference between these two nodes for IP=0 is maximum (25mV , 2.475<VOUT<2.525V  ③The primary winding is with 3 wires parallel.

Remarks

- VOUT is positive when Ip flows from terminals 1,2,3 to terminals 4,5,6

- This is a standard model .For different versions (supply voltages,turns ratios,unidirectional

measurements….), please contact us.

# Text boxes

IPN = 25 A

Applications

- AC variable speed drives and servo motor drives

- Static converters for DC motor drives

- Battery supplied applications

- Uninterruptible Power Supplies(UPS)

- Switched Mode Power Supplies (SMPS)

- Power supplies for welding applications.

Features

- Closed loop (compensated) current transducer using the Hall-Effect

Advantages

- Excellent accuracy

- Very good linearity

- Low temperature drift

Special features

- Printed circuit board mounting.

- Unipolar voltage supply.