Current Transducer CH-O-0001-0401

* CH-O-0001-0401 is a Hall-Effect current transducer.

* It is used for the detection of DC ,AC ,pulse.

| Electrical data |
| --- |
| IPN | Primary nominal r.m.s current | 350 | mA |
| IP | Primary current, measuring range | ( 700 | mA |
| VC | Supply voltage (( 5%) | +5 | V |
| IC | Idle current consumption | <±20 | mA |
| Vd | AC isolation test, 50/60 Hz, 1min RM max | 3 | kV |
| RIS | Isolation resistance @ 500 VDC | >500 | M( |
| VOUT | Output voltage @ ( IPN, RL = 10 k(, TA = 25(C | 0...±2 | V |
| RL | Load resistance | (10 | k( |

| Accuracy – Dynamic performance data |
| --- |
| X | Accuracy @ IPN , TA = 25(C (without offset) | < ( 1 | % |
| (L | Linearity (0.. ( IPN) | <( 1 | %of IPN |
| VOE | Electrical offset voltage ,TA = 25(C @(100 Amax 0 0 | <(20 | mV |
| VOH | Hysteresis offset voltage @ IP = 0; |  |  |
|  | after an excursion of 3 ( IPN | < ( 30 | mV |
| VOT | Thermal drift of VOE | <( 1 | mV/℃ |
| tr | Response time @ 90% of IP | <3 | (s |
| di/dt | di/dt accurately followed | >100 | A/(s |
| f | Frequency bandwidth (-3 dB) | 3 | kHZ |

| General data |
| --- |
| TA | Ambient operating temperature |  | - 20 ... + 80 | (C |
| m | Mass |  |  | g |

Direction of use:

Precaution -  Output voltage: 0 ~ (2V.

Or output current: 0～20mA.

If the above-stated condition is fulfilled, go to following steps:

Put the conducting wire through the center hole of the current transducer.

Connected the transducer as the pictures shown.

# Text boxes

Applications

- AC motor speed control.

- Static converters for DC motor drives.

- Battery supplied applications.

- Uninterruptible Power Supplies (UPS).

- Power supplies for welding, cable TV and telecommunication applications.

Advantages

- Easy mounting.

- Small size and space savings.

- Only one design for wide current ratings range.

- High immunity against external interference.

- Current overload capability.

IPN = 350mA

VOUT = 0…(2V

Features

- Hall effect measuring principle.

- Galvanic isolation between primary and secondary circuit.

- Low power consumption.

- Printed circuit board mounting.