CH-O-0400-1403                   * CH-O-(0100~0600)-1403 is a Hall-Effect current transducer.

Current Transducer                            * It can be used for the detection of DC, AC, pulse.

| Electrical data |
| --- |
| IPN | Primary nominal r.m.s current |  |  |  | 400 | A |
| IP | Primary current, measuring range |  |  |  | ( 1000 | A |
| IOUT | Output current @TA = 25(C AC current | 4…20 | mA |
|  | DC current | 4…20 | mA |
| VC | Supply voltage (( 5%) | (20…36 | V |
| IC | Idle current consumption | < 20 | mA |
| Vd | AC isolation test, 50 Hz, 1min RM max | 2.5 | kV |
| RL | Load resistance | ≥300 | ( |

| Accuracy – Dynamic performance data |
| --- |
| X | Accuracy @ IPN , TA = 25(C (without offset) | < ( 1 | % |
| (L | Linearity (0.. ( IPN) | ( ( 1 | %of IPN |
| IOE | Electrical offset current @ IP = 0, TA = 25(C @(100 Amax 0 0 | < ( 0.15 | mA |
| IOH | Hysteresis offset current @ IP = 0; |  |  |
|  | after an excursion of 3 ( IPN | < ( 0.15 | mA |
| IOT | Thermal drift of IOE (-10℃…+100℃) | ( 0.40 | mA |
| tr | Response time @ 90% of IP | < 10 | (s |
| di/dt | di/dt accurately followed | > 50 | A/(s |
| f | Frequency bandwidth (-3 dB) | DC…50 | kHz |

| General data |
| --- |
| TA | Ambient operating temperature |  | -10..+100 | (C |
| m | Mass |  | 136 | g |

Direction of use:

Precaution -	Nominal current measuring range: 100 A ~ 600 A (AC) or 100 A ~ 600 A (DC).

Or output current:4～20mA.

If the above-stated condition is fulfilled, go to following steps:

Put the conducting wire through the center hole of the current transducer.

Connected the transducer as the pictures shown.

Adjust the OFS to obtain a zero offset output voltage if offset is non-zero. (EX-Factory is zero offset)

Adjust the GIN to obtain a desire maximum output voltage. (EX-Factory is 4V typical)

# Text boxes

IPN =100…600A

Applications

- AC motor speed control.

- Static converters for DC motor drives.

- Battery supplied applications.

- Uninterruptible Power Supplies (UPS).

- Power supplies for welding, cable TV and telecommunication applications.

Advantages

- Easy mounting.

- Small size and space savings.

- Only one design for wide current ratings range.

- High immunity against external interference.

- Current overload capability.

- Adjustable output gain.

- Adjustable offset to zero.

Features

- Hall effect measuring principle.

- Galvanic isolation between primary and secondary circuit.

- Low power consumption.

### SECONDARY  TERMINALS

TERMINAL +:  SUPPLY VOLTAGE +20…36V

TERMINAL -:  SUPPLY VOLTAGE – 20…36V

TERMINAL  OUT : OUTPUT MEASURE

TERMINAL 0:  0V

## Adjustment

#### OFS  : Zero offset adjust

GIN  : Output amplitude adjust